## Slide 1: CSE-425 Lecture-2 Reference: Second chapter of textbook Acknowledgment: Some websites and Chung-Ping Young from Dept. of Computer Science and Information Engineering, National Cheng Kung University, TAIWAN

## Slide 2: Lecture Objective
Upon completion of this lecture, the students will be able to:
Determine criteria before considering a microcontroller
Compare and contrast the various members of the AVR family

## Slide 3: Microcontrollers for Embedded system
What is an embedded system?
An embedded system is a microprocessor-based computer hardware system with software that is designed to perform a dedicated function, either as an independent system or as a part of a large system. At the core is an integrated circuit designed to carry out computation for real-time operations.
Complexities range from a single microcontroller to a suite of processors with connected peripherals and networks; from no user interface to complex graphical user interfaces. The complexity of an embedded system varies significantly depending on the task for which it is designed.
Embedded system applications range from digital watches and microwaves to hybrid vehicles. As much as 98 percent of all microprocessors manufactured are used in embedded systems.

## Slide 4: Basic Structure of an Embedded System:
The basic structure of an embedded system includes the following components:
Sensor: The sensor measures and converts the physical quantity to an electrical signal, which can then be read by an embedded systems engineer or any electronic instrument. A sensor stores the measured quantity to the memory.
A-D Converter: An analog-to-digital converter converts the analog signal sent by the sensor into a digital signal.
Processor: Processors assess the data to measure the output and store it to the memory.
D-A Converter: A digital-to-analog converter changes the digital data fed by the processor to analog data
Actuator: An actuator is a device that produces a motion by converting energy and signals going into the system. The motion it produces can be either rotary or linear.

## Slide 5
Embedded system:
An embedded product uses a microprocessor (or microcontroller) to do one task and one task only
There is only one application software that is typically burned into ROM
General-purpose system:
A PC, in contrast with the embedded system, can be used for any number of applications.
It has RAM memory and an operating system that loads a variety of applications into RAM and lets the CPU run them
A PC contains or is connected to various embedded products and each one peripheral has a microcontroller inside it that performs only one task

## Slide 6
Home:
Appliances, intercom, telephones, security systems, garage door openers, answering machines, fax machines, home computers, TVs, cable TV tuner, VCR, camcorder, remote controls, video games, cellular phones, musical instruments, sewing machines, lighting control, paging, camera, pinball machines, toys, exercise equipment
Some Embedded Products Using Microcontrollers:
Auto:
Trip computer, engine control, air bag, ABS, instrumentation, security system, transmission control, entertainment, climate control, cellular phone, keyless entry
Office:
Telephones, computers, security systems, fax machines, microwave, copier, laser printer, color printer, paging

## Slide 7: Criteria for Choosing a microcontroller:
The most important factor is that the microcontroller should be cost-efficient and work capably to handle the dedicated task. Some questions that should be asked while deciding on a microcontroller are as follows:
  1. What is the maximum speed of the microcontroller?
  2. What is the amount of RAM and ROM on chip?
  3. How easy it is to upgrade to higher upgrade or lower consumption versions?
  4. Is the microcontroller readily available at cheaper rates?
  5. What is the number of I/O pins and timer on the chip?

## Slide 8: Criteria for Choosing a microcontroller:
Meeting the computing needs of the task at hand efficiently and cost effectively
  Speed
  Packaging
  Power consumption
  The amount of RAM and ROM on chip
  The number of I/O pins and the timer on chip
  How easy to upgrade to higher performance or lower power-consumption versions
  Cost per unit

## Slide 9: Overview of the AVR family
A brief history of the AVR microcontroller:
The basic architecture of AVR was designed by two students of Norwegian Institute of Technology(NTH), Alf-Egil Bogen and Vegard Wollan and then was bought and developed by Atmel in 1996.
One might wonder what AVR stands for! AVR can have different meanings for different people! According to Atmel, it is nothing more than a product name but it might stands for Advanced Virtual RISC or Alf and Vegard RISC.
There are many kinds of AVR microcontroller with different properties.
One of the problems with the AVR microcontrollers is that they are not all 100% compatible in terms of software. To run programs written for the ATtiny25 on a ATmega64, we must recompile the program and possibly change some register locations before loading it into the ATmega64.

## Slide 10: What’s special about AVR?
They are fast. An AVR microcontroller executes most of the instructions in single execution cycle. AVRs are about 4 times faster than PICs, they consume less power and can be operated in different power saving modes. Let’s do the comparison between the three most commonly used families of microcontrollers:
Criteria | 8051 | PIC | AVR
SPEED | Slow | Moderate | Fast
MEMORY | Small | Large | Large
ARCHITECTURE | CISC | RISC | RISC
ADC | Not Present | Inbuilt | Inbuilt
Timers | Inbuilt | Inbuilt | Inbuilt
PWM Channels | Not Present | Inbuilt | Inbuilt

## Slide 11: Overview of the AVR family
AVR can be classified into four groups:
Classic AVR (AT90Sxxxx): The original AVR chip, which has been replaced by newer AVR chips. For new designs, they are not recommended. Like: AT90S2313, AT90S2323, AT90S4433
Mega AVR (ATmegaxxxx): Powerful microcontrollers with more than 120 instructions and lots of different peripheral capabilities which can be used in different designs. These are the most popular ones having good amount of memory (upto 256 KB), higher number of inbuilt peripherals and suitable for moderate to complex applications.
Tiny AVR (ATtinyxxxx): Less memory, small size, suitable only for simpler applications. Like ATtiny13, ATtiny25, ATtiny44
Special purpose AVR: The IC’s of this group can be considered as a subset of other groups but their special capabilities are made for designing specific applications like USB controller, LCD controller etc. Example: ATmega169, AT90CAN128, AT90USB1287, AT90PWM216

## Slide 12: AVR features
AVR is an 8-bit RISC single-chip microcontroller Harvard architecture that comes with some standard features like:
On-chip program (code) ROM
Data (RAM)
Data (EEPROM)
Timer
I/O ports
Interrupt
Most AVRs have some additional features like ADC, PWM, different kind of serial interface like USART, SPI, I2C (TWI), CAN, USB and so on.

## Slide 13
Program ROM
RAM
EEPROM
Timers
CPU
OSC
Interrupt Unit
I/O Ports
Other Peripherals
A simplified view of an AVR Microcontroller:

## Slide 14: Features of ATmega32
• High-performance, Low-power AVR® 8-bit Microcontroller
• Advanced RISC Architecture
  – 131 Powerful Instructions
  – Most Single-clock Cycle Execution
  – 32 x 8 General Purpose Working Registers
  – Fully Static Operation
• High Endurance Non-volatile Memory segments
  – 32K Bytes of In-System Self-programmable Flash program memory
  – 1024 Bytes EEPROM
  – 2K Byte Internal SRAM
  – Write/Erase Cycles: 10,000 Flash/100,000 EEPROM
  – Data retention: 20 years at 85°C/100 years at 25°C(1)
  – Programming by On-chip Boot Program True Read-While-Write Operation
  – Programming Lock for Software Security

## Slide 15: Features of ATmega32
• Peripheral Features
  – Two 8-bit Timer/Counters with Separate Prescalers and Compare Modes
  – One 16-bit Timer/Counter with Separate Prescaler, Compare Mode, and Capture Mode
  – Real Time Counter with Separate Oscillator
  – Four PWM Channels
  – 8-channel, 10-bit ADC 8 Single-ended Channels 7 Differential Channels in TQFP Package Only 2 Differential Channels with Programmable Gain at 1x, 10x, or 200x
  – Byte-oriented Two-wire Serial Interface
  – Programmable Serial USART
  – Master/Slave SPI Serial Interface
  – Programmable Watchdog Timer with Separate On-chip Oscillator
  – On-chip Analog Comparator

## Slide 16: Features of ATmega32
• Special Microcontroller Features
  – Power-on Reset and Programmable Brown-out Detection
  – Internal Calibrated RC Oscillator
  – External and Internal Interrupt Sources
  – Six Sleep Modes: Idle, ADC Noise Reduction, Power-save, Power-down, Standby and Extended Standby
• I/O and Packages
  – 32 Programmable I/O Lines
  – 40-pin PDIP, 44-lead TQFP(Quad Flat package), and 44-pad QFN/MLF(Quad flat no lead/ Micro lead Frame package)
• Operating Voltages
  – 2.7 - 5.5V for ATmega32L
  – 4.5 - 5.5V for ATmega32

## Slide 17: Features of ATmega32
• Speed Grades
  – 0 - 8 MHz for ATmega32L
  – 0 - 16 MHz for ATmega32
• Power Consumption at 1 MHz, 3V, 25°C for ATmega32L
  – Active: 1.1 mA
  – Idle Mode: 0.35 mA
  – Power-down Mode: < 1 μA

## Slide 18: Features of ATmega8
• High-performance, Low-power AVR® 8-bit Microcontroller
• Advanced RISC Architecture
  – 130 Powerful Instructions
  – Most Single-clock Cycle Execution
  – 32 x 8 General Purpose Working Registers
  – Fully Static Operation – Up to 16 MIPS Throughput at 16 MHz
  – On-chip 2-cycle Multiplier
• High Endurance Non-volatile Memory segments
  – 8K Bytes of In-System Self-programmable Flash program memory
  – 512 Bytes EEPROM
  – 1K Byte Internal SRAM
  – Write/Erase Cycles: 10,000 Flash/100,000 EEPROM – Data retention: 20 years at 85°C/100 years at 25°C(1)
  – Optional Boot Code Section with Independent Lock Bits In-System Programming by On-chip Boot Program True Read-While-Write Operation
  – Programming Lock for Software Security

## Slide 19: Features of ATmega8
• Peripheral Features
  – Two 8-bit Timer/Counters with Separate Prescaler, one Compare Mode
  – One 16-bit Timer/Counter with Separate Prescaler, Compare Mode, and Capture Mode
  – Real Time Counter with Separate Oscillator
  – Three PWM Channels
  – 8-channel ADC in TQFP and QFN/MLF package Eight Channels 10-bit Accuracy
  – 6-channel ADC in PDIP package Six Channels 10-bit Accuracy
  – Byte-oriented Two-wire Serial Interface
  – Programmable Serial USART
  – Master/Slave SPI Serial Interface
  – Programmable Watchdog Timer with Separate On-chip Oscillator
  – On-chip Analog Comparator

## Slide 20: Features of ATmega8
• Special Microcontroller Features
  – Power-on Reset and Programmable Brown-out Detection
  – Internal Calibrated RC Oscillator
  – External and Internal Interrupt Sources
  – Five Sleep Modes: Idle, ADC Noise Reduction, Power-save, Power-down, and Standby
• I/O and Packages
  – 23 Programmable I/O Lines
  – 28-lead PDIP, 32-lead TQFP, and 32-pad QFN/MLF
• Operating Voltages
  – 2.7 - 5.5V (ATmega8L)
  – 4.5 - 5.5V (ATmega8)

## Slide 21: Features of ATmega8
• Speed Grades
  – 0 - 8 MHz (ATmega8L)
  – 0 - 16 MHz (ATmega8)
• Power Consumption at 4 Mhz, 3V, 25°C
  – Active: 3.6 mA
  – Idle Mode: 1.0 mA
  – Power-down Mode: 0.5 μA

## Slide 22
The mega AVR family:
Part Name | ROM | RAM | EEPROM | I/0 Pins | Timer | Interrupts | Operation Voltage | Operating frequency | Packaging
ATmega8 | 8KB | 1KB | 512B | 23 | 3 | 19 | 4.5-5.5 V | 0-16 MHz | 28
ATmega8L | 8KB | 1KB | 512B | 23 | 3 | 19 | 2.7-5.5 V | 0-8 MHz | 28
ATmega16 | 16KB | 1KB | 512B | 32 | 3 | 21 | 4.5-5.5 V | 0-16 MHz | 40
ATmega16L | 16KB | 1KB | 512B | 32 | 3 | 21 | 2.7-5.5 V | 0-8 MHz | 40
ATmega32 | 32KB | 2KB | 1KB | 32 | 3 | 21 | 4.5-5.5 V | 0-16 MHz | 40
ATmega32L | 32KB | 2KB | 1KB | 32 | 3 | 21 | 2.7-5.5 V | 0-8 MHz | 40